## Slide 1
Logical Block Diagram
Master Controller
Left Panel
Panel 7
Panel 8
Panel 5
Panel 6
Panel 3
Panel 4
Panel 1
Panel 2
Panel Control Microprocessor
Right Panel
Panel 7
Panel 8
Panel 5
Panel 6
Panel 3
Panel 4
Panel 1
Panel 2
Panel Control Microprocessor
Master Control Microprocessor
(Arduino Nano)
DS3231 Real Time Clock
NRF24L01+PA Radio
16 Pin (2x8) Ribbon Cable
I2C Serial Bus
I2C Serial Bus
2.4GHz Coax
8 Pin (2x4) Cable

## Slide 2
Power Block Diagram
Master Controller
Master Control Microprocessor
DS3231 Real Time Clock
NRF24L01+PA Radio
Left Panel
Panel 7
Panel 8
Panel 5
Panel 6
Panel 3
Panel 4
Panel 1
Panel 2
Panel Control Microprocessor
240V AC - 5V 40A DC POWER
Right Panel
Panel 7
Panel 8
Panel 5
Panel 6
Panel 3
Panel 4
Panel 1
Panel 2
Panel Control Microprocessor
240V AC - 5V 40A DC POWER
LM117 3V3 Regulator
3V DC
5V DC
240V AC

## Slide 3
Sponsors Board
Sponsor Panel
Huidu HD-W6B LED Controller
HD2020 Software
240V AC - 5V 40A DC POWER
Panel B1
Panel B2
Panel B3
Panel B4
Panel B5
Panel B6
Panel B7
Panel A1
Panel A2
Panel A3
Panel A4
Panel A5
Panel A6
Panel A7
Panel C1
Panel C2
Panel C3
Panel C4
Panel C5
Panel C6
Panel C7
240V AC - 5V 40A DC POWER
240V AC - 5V 40A DC POWER
16 Pin Ribbon
5V DC
Ethernet